## Slide 1: A YANG Data Model for Network Hardware Inventory
CCAMP WG, IETF116
draft-ietf-ccamp-network-inventory-yang-01
Authors:
Chaode Yu (yuchaode@huawei.com)
Italo Busi (Italo.Busi@huawei.com)
Aihua Guo (aihuaguo.ietf@gmail.com)
Sergio Belotti(sergio.belotti@nokia.com)
Jean-Francois Bouquier(jeff.bouquier@vodafone.com)
Fabio Peruzzini(fabio.peruzzini@telecomitalia.it)
Oscar Gonzalez de Dios(oscar.gonzalezdedios@telefonica.com)
Victor Lopez(victor.lopez@nokia.com)
Chenfang Zhang(zhangcf80@chinaunicom.com)

## Slide 2: UC1. Central View of Asset Management
Service Provisioning OSS
Construction
OSS
Resource Management OSS
Customer Management OSS
APP
Network Controller
Alarm/PM Monitoring OSS
Service Provisioning: RESTCONF
Inventory:
Corba/XML/RESTCONF
Alarm & PM:
XML/TXT/RESTCONF
Service Order
Construction order
BSS
Resource Validation
Resource Retrieval
Service Retrieval & Update:
RESTCONF & Notification
Planning OSS
Resource Mapping
Network
To be simplified to focus only on the OSS systems which are relevant for the inventory use cases (issue #69)

## Slide 3: Major Updates Since IETF 115
Adopted as WG document in January 2023
Draft updates
  Addressed most of the comments from WG adoption poll with thre remaning issues:
    clarify why not augmenting RFC8345 (issue #14)
    equipment room versus site
    inventory for software components (issue #64)
  Name of the model updated to match its scope: ietf-network-hardware-inventory
  Text updated to align with the scope (network hardware inventory)
  Fixed reference to TMF document
  Fixed the number of authors to comply with RFC7322
  Added a YANG model for navigation from topology to inventory
  Few other changes to YANG
    Removed rack-number in rack and firmware-rev in NE
    Added relative-position of chassis in rack
    Removed equipment room, rack and NE info in the component's parent reference structure

## Slide 4: Navigation from Topology to Inventory
Network Hardware Inventory YANG
Network Topology YANG
Inventory/Topology Ref YANG
augments
references
(ietf-hw-inventory-ref-topo)
Topology |  | Hardware Inventory
Node |  | Network Element
Link Termination Point (LTP) |  | Port component
Link |  | Fiber/Cable (to be added)

## Slide 5
Improve definitions of the location information
Equipment room location: two options
  The postal/street address -> to be clarified
  The GIS location (re-using the grouping in RFC9179) -> to be added
Rack location
  The rack row and column number within the equipment room (physical)
Chassis relative position
  The physical position of the chassis within the rack
NE location
  The equpment room(s) where the components of the NE are located
Component location
  The relative position of a component within the NE -> to be clarified
  Typical format for Optical NEs:
    /ne=<ne_name>[/r=<r_index>][/sh=<sh_index>[/s_sh=<s_sh_index> ...]][[/sl=<sl_index>[/s_sl=<s_sl_index> ...]][/p=<p_index> …]]

## Slide 6
Component Location
Defined as a free-format string (in alignment with Openconfig)
  Typical format for Optical NEs:
    /ne=<ne_name>[/r=<r_index>][/sh=<sh_index>[/s_sh=<s_sh_index> ...]][[/sl=<sl_index>[/s_sl=<s_sl_index> ...]][/p=<p_index> …]]
  Which format is used for IP or MW NEs?
Difference between chassis component location and relative position:
rack
ne-foo
main shelf
1
2
3
Chassis relative position: 2
Chassis component location: ne=ne-foo/sh=1

## Slide 7
Next Steps
Provide some equipment configuration examples
  Get more input from IP and microwave technologies
Identify some more component-specific attributes and introduce more component types
Progressing to fix the remaining issues
Welcome to join our weekly discussion
Meeting slot: Wednesday 3-4pm CET (9-10am EST)
Github: https://github.com/italobusi/ietf-network-inventory

## Slide 8
Thank You ！