## Slide 1: A YANG Data Model for Network Hardware Inventory
CCAMP WG, IETF116
draft-ietf-ccamp-network-inventory-yang-01
Authors:
Chaode Yu (yuchaode@huawei.com)
Italo Busi (Italo.Busi@huawei.com)
Aihua Guo (aihuaguo.ietf@gmail.com)
Sergio Belotti(sergio.belotti@nokia.com)
Jean-Francois Bouquier(jeff.bouquier@vodafone.com)
Fabio Peruzzini(fabio.peruzzini@telecomitalia.it)
Oscar Gonzalez de Dios(oscar.gonzalezdedios@telefonica.com)
Victor Lopez(victor.lopez@nokia.com)
Chenfang Zhang(zhangcf80@chinaunicom.com)

## Slide 2: UC1. Central View of Asset Management
Resource Management OSS
Network Controller
Network
Other
OSS
Resource Mapping
Service Provisioning
Alarm/PM
Resource Retrieval
Resource Validation
BSS
Customer-oriented APP
Network Hardware Inventory

## Slide 3: Updates Since IETF 115
Adopted as WG document in January 2023
Draft updates
  Addressed most of the comments from WG adoption poll with three remaning issues:
    clarify why not augmenting RFC8345 (issue #14)
    equipment room versus site
    inventory for software components (issue #64)
  Name of the model updated to match its scope: ietf-network-hardware-inventory
    Text updated to align with the scope (network hardware inventory)
  Fixed reference to TMF document
  Fixed the number of authors to comply with RFC7322
  Added a YANG model for navigation from topology to inventory
  Few other changes to YANG
    Removed rack-number in rack and firmware-rev in NE
    Added relative-position of chassis in rack
    Removed equipment room, rack and NE info in the component's parent reference structure

## Slide 4: Why not augmenting Network YANG (RFC8345)
Hardware Inventory and Network Topology are different concepts
  Hardware inventory is used for asset management
  Network topology represents logical resources used for service provisioning
Defining a new root avoids the need for the client to do some filtering to recognize the network-id of the hardware inventory network instance
No real advantages on re-using Network YANG model
  Navigation from Network Topology and Network Hardware Inventory models requires anyhow some augmentations to the Network Topology YANG model (see next slide)

## Slide 5: Navigation from Topology to Inventory
Network Hardware Inventory YANG
Network Topology YANG
Inventory/Topology Ref YANG
augments
references
(ietf-hw-inventory-ref-topo)
Topology |  | Hardware Inventory
Node |  | Network Element
Link Termination Point (LTP) |  | Port component
Link |  | Fiber/Cable (to be added)
Do we need to reference other type of inventory object? To be checked by examples

## Slide 6
Improve definitions of the location information
Equipment room location: two options
  The postal/street/... address -> to be clarified (see e.g., RFC 8299)
  The GIS location (re-using the grouping in RFC9179) -> to be added
Rack location
  The physical location of the rack within the equipment room (row and column)
Chassis relative position
  The physical position of the chassis within the rack
NE location
  The equpment room(s) where the components of the NE are located
Component location
  See next slide

## Slide 7
Component Location
The relative/logical position of a component within the NE -> to be clarified
Defined as a free-format string (in alignment with Openconfig)
  Typical format for Optical NEs:
    /ne=<ne_name>[/r=<r_index>][/sh=<sh_index>[/s_sh=<s_sh_index> ...]][[/sl=<sl_index>[/s_sl=<s_sl_index> ...]][/p=<p_index> …]]
  Is there a normative reference defining this typical format?
  Which format is used for IP or MW NEs?

## Slide 8
Chassis component location and relative position
Chassis relative position: 2
component location: ne=ne-foo/sh=1
Chassis relative position: 3
component location: ne=ne-foo/sh=2
rack A
ne-foo
second shelf
1
2
3
rack B
ne-foo
main-shelf
1
2
3

## Slide 9
Next Steps
Continue coordination work with other inventory models (OPS area)
Provide some equipment configuration examples
  Get more input from IP and microwave vendors/operators
Identify some more component-specific attributes and introduce more component types
Progressing to fix the remaining issues
Welcome to join our weekly discussion
Meeting slot: Wednesday 3-4pm CEST (9-10am EDT)
Github: https://github.com/ietf-ccamp-wg/ietf-network-inventory

## Slide 10
Thank You ！